## Slide 1
drilling rig

## Slide 2
Derrick
This structure above the well for conducting STR, placement of drill candles, is the basis for the placement and installation of drilling equipment. There are two types of towers: tower and mast. They are made of pipes or rolled steel. The tower is a regular truncated tetrahedral pyramid of lattice construction. Mast-type towers are single-support and double-support (A-shaped). The latter are the most common. A - shaped towers are more labor intensive and less stable, but they are easier to transport from place to place and assemble / disassemble.

## Slide 3
Drilling winch
The drilling winch is designed for lowering and lifting the drill string, screwing and unscrewing the pipes, lowering the casing strings, holding the fixed string on the weight or slowing it down (feeding) while drilling.
In some cases, the drawworks is used to transfer power from the engine to the rotor, dragging cargo and other auxiliary works.

## Slide 4
Crown block
Crown block is a frame on which axles and supports with pulleys are mounted. Sometimes the frame is made as one piece with the upper part of the tower.

## Slide 5
Waist block
The waist block represents the welded case in which pulleys and bearing knots are located.

## Slide 6
Waist ropes
Waist ropes are steel round, six-row ropes of cable construction of cross-lay. Strands twisted into a rope around an organic or metal core are made of high-carbon and high-manganese steel of high strength with a number of wires from 19 to 37. Taking into account the attachment point of the running end of the rope in the direction of winding it on the drum, right-twisted rope diameters of 25 diameters are used for drilling winches , 28, 32, 35, 38 mm. The most common ropes with organic and plastic core diameters of 28 and 32 mm. At depths of more than 4000m, cables with a metal core are used.

## Slide 7
Drilling hooks and hook blocks
Drilling hooks and hook blocks are designed for hanging on them in the process of drilling drilling tools and elevators during tripping operations.
Hook blocks (hooks connected to the pulley block) have several advantages: a smaller overall height than that of the pulley block and hook combined, a more compact design. The disadvantages include their large mass.

## Slide 8
Drill lines
Drill lines are the links connecting the hook to the elevator, on which the drilling tool or casing string is suspended. Load capacity of bails - 25, 50.75, 125, 200 and 300 tons.

## Slide 9
Elevator
Elevator - designed to capture and hold on the weight of the drill string or casing during tripping operations. Elevators of various types are used, differing in size depending on the diameter of the drill or casing pipes, carrying capacity, design and material for their manufacture.

## Slide 10
Wedges
Wedges - for drill pipes are used to hang the drilling tools in the rotor table. They are inserted into the tapered hole between the tube and the rotor liners. The use of wedges speeds up tripping operations. Casing wedges are used for launching heavy casing. Pneumatic rotary wedge grip (RCC), built into the rotor and is designed for raising and lowering wedges.

## Slide 11
Drill keys
For screwing and unscrewing the drill and casing pipes used various keys. Some of them are intended for screwing, while others are used for fastening and unfastening the threaded connections of the column. Usually, lightweight circular wrenches for preliminary screwing up of pipes are designed for locks of the same diameter, and heavy machine keys for fastening and unfastening threaded connections — for two, and sometimes more sizes for drill pipes and locks. The operation of fastening and detaching the threaded connections is carried out by two machine keys: one key (retaining) - fixed, and the second - (screwing or detaching) - movable. Keys are hung horizontally and attached to steel ropes to facilitate their movement. Work on the descent and ascent is greatly facilitated by using the automatic drill key battery, installed between the winch and the rotor.

## Slide 12
Rotor
Rotor - designed to transmit rotational motion of the string of drill pipe in the drilling process, keeping it on weight during tripping and auxiliary operations. The rotor is a gearbox that transmits the rotation of a vertically suspended string of drill pipes from a horizontal shaft of a transmission transmission.

## Slide 13
Swivel
Swivel - designed to connect the pulley system with a drill string. It ensures the rotation of the drill string suspended on the hook and the supply of flushing fluid through it.

## Slide 14
Drilling hoses
Drilling hoses are made of rubberized fabric with an appropriate number of intermediate layers of rubber, metal films and the outer layer of rubber. For pressures above 30 MPa use metal hoses, consisting of separate sections, pivotally connected to each other.

## Slide 15
Drill bit
Drill bit - the main element of the drilling tool for the mechanical destruction of rock at the bottom of the well in the process of its penetration

## Slide 16
Now answer the questions
1) Where is the swivel?

## Slide 17
2) Where is the drilling hoses?

## Slide 18
3) Where is the wedges?

## Slide 19
4) Where is the drill bit?

## Slide 20
5) Where is the crown block?

## Slide 21
6) Where is the waist block?

## Slide 22
What is it?
Wedges
Elevator
Crown block
Drill keys

## Slide 23
What is it?
Drill bit
Drilling hoses
Drilling winch
Swivel

## Slide 24
What is it?
Rotor
Drill bit
Elevator
Crown block

## Slide 25
What is it?
a) Waist ropes
b) Rotor
c) Drill bit
d) Drilling hooks

## Slide 26
What is it?
Rotor
Elevator
Crown block
Waist block

## Slide 27
What is it?
Swivel
Rotor
Drill bit
Elevator

## Slide 28
Repeat previously studied material
Derrick – Буровая вышка
Drilling winch – Буровая лебедка
Crown block – Кронблок
Waist block – Талевый блок
Waist ropes – Талевые канаты
Drilling hooks and hook blocks – Буровые крюки и крюкоблоки
Drill lines – Бурильные штропы
Elevator – Элеватор
Wedges – Клинья
Drill keys – Буровые ключи
Rotor – Ротор
Swivel – Вертлюг
Drilling hoses – Буровые шланги
Drill bit – Долото