## Slide 1: The main types of modern lathes

## Slide 2
Modern lathes are highly efficient, accurate and complex devices, capable of doing a great quantity and variety of work. Lathes are made in a wide variety of types and sizes, from the small precision lathe found in watch repair shops to the immense machine.
The lathe consists essentially of a bed (1), headstock,(2) tailstock(4) and saddle(3).
Lathe

## Slide 3
1.bed
2.head-
stock
3.saddle
4.tailstock

## Slide 4
Turret Lathe – The characteristic feature of a turret lathe is the turret which is mounted upon a carriage and contains the tools which are successively brought into the working position by indexing or rotating the turret. Many turret lathes also have systems of stops or gauges for controlling the travel of the turret carriage and
cross-slide, in order
to regulate the
depth of a bored
hole, the length
of a cylindrical
part or its diameter.
Turret lathe

## Slide 5
Drilling machines
Drilling machines which are used mainly for drilling holes in machine parts, are made in many different types designed for handling the various classes of work.
The upright drilling machine is the type most commonly used, and the name applied to this class indicates that the general design of the machine is vertical and also that the drill spindle is in a vertical position.
The multiple-spindle type is built in both vertical and horizontal design.
It can perform a number of operations on a component without the necessity of changing tools.
Gang Drills – When a number of single-spindle drilling machine columns are placed side by side on a common base and have a common work table, the machine is known as a gang drill. Each spindle is independently controlled as to speed and feed so that a number of operations may be performed is succession and simultaneously upon the machine. In this machine work is moved progressively from one spindle to the next.

## Slide 6
The radial drilling machine – The main advantage of a radial machine is that the drill can be moved over the work to any desired position, so that a large number of holes can be drilled in the work without moving it.
The sensitive drill
is a small machine of light
construction, which possesses
sensitive qualities which are
of value in drilling holes
in delicate work.
Radial drilling machine

## Slide 7
Drilling machines which are used mainly for drilling holes in machine parts, are made in many different types designed for handling
the various classes
of work. The upright
drilling machine
is the type most
commonly used, and
the name applied to
this class indicates that
the general design of
the machine is vertical
and also that the drill
spindle is in a vertical
position.
Upright drilling machine

## Slide 8
A shaper is a machine that forms surfaces by successive reciprocating cuts of a tool over the work. The work is stationary with reference to the tool but moves laterally in small steps so that the successive cuts can be made. Although most of the work performed on shapers consists of plane horizontal surfaces, it is also possible to finish vertical and angular surfaces, and, with the proper tools and accessories, even curved surfaces may be machined.
The size of a shaper is determined by the longest stroke of the ram. Shapers are driven by belt from a countershaft, by direct connected motor, or by hydraulic power.
Shaper

## Slide 9
Planers
Planers are essentially for machining plane surfaces which are larger than can be cut or reached on the shaper. The modern planer with modern electric controls has a high output.
The planer has a reciprocating table which travels beneath a cross bar on which the tool heads are mounted. Normally one or two tool heads are mounted on the cross bar, but additional tools, generally for cutting vertical faces, may be mounted on the columns supporting the cross bar. The usual design comprises two vertical columns between which the table reciprocates. The cross bar is so mounted that it can slide vertically on these columns. All motions for feed or cut take place either by dropping the cross bar, moving the tool head across the cross bar, or lowering the tool holder mounted on the tool head. The first two of these motions are generally power or hand-operated but the last is often hand-operated only.
The table is normally operated by some form of rack-and-pinion or spiral drive. Modern high-speed planers are now fully electrified.

## Slide 10
Slotters are usually provided with three or four speeds, btained either by cone pulley or gear-box. The work table is usually circular and provided with T-slots for clamping the work. The slotting machine may be looked upon as a vertical shaping
machine. It machines the
Internal surfaces of a
Casting or forging and
can do circular work by
Virtue of its pivoted table.
Originally slotters
were used for cutting
keyways, machining the
square holes in such
parts as dog clutches
and they are still used
for this work in small shops.
Slotter